## Slide 1: Introduction to Operating Systems
Spring 2018 Lecture Notes
Chapters 11 and 12
adapted from Tom Anderson’s slides on OSPP web site

## Slide 2: Storage Systems

## Slide 3: Main Points
File systems
  Useful abstractions on top of physical devices
Files
  Metadata, data, file types, open/close
Storage hardware characteristics
  Disks and flash memory
File system usage patterns
Naming

## Slide 4: File Systems
Abstraction on top of persistent storage
  Magnetic disk
  Flash memory (e.g., USB thumb drive)
Devices provide
  Storage that (usually) survives across machine crashes
  Block level (random) access
  Large capacity at low cost
  Relatively slow performance
    Magnetic disk read takes 10-20M processor instructions

## Slide 5: File System as Illusionist: Hide Limitations of Physical Storage
Persistence of data stored in file system:
  Even if crash happens during an update
  Even if disk block becomes corrupted
  Even if flash memory wears out
Naming:
  Named data instead of disk block numbers
  Directories instead of flat storage
  Byte addressable data even though devices are block-oriented
Performance:
  Cached data
  Data placement and data structure organization
Controlled access to shared data

## Slide 6: I/O System Layers

## Slide 7: Logical Record Blocking
Application
Device
Physical record buffer
Reads/writes of
logical records
(can be 1 byte at a time)
Reads/writes of
physical records (blocks)
(1000s of bytes at a time)
Buffer in memory reduces the number of physical I/O ops
Note: double-buffering allows processing to overlap transfer of next physical record

## Slide 8: File System Abstraction
File system
  Persistent, named data
  Hierarchical organization (directories, subdirectories)
  Access control on data
File: named collection of data
  Linear sequence of bytes (or a set of sequences)
  Read/write or memory mapped
Crash and storage error tolerance
  Operating system crashes (and disk errors) leave file system in a valid state
Performance
  Achieve close to the hardware limit in the average case

## Slide 9: Files
Metadata
  owner, access permissions, timestamps (creation, last written), size, reference count, lock, etc.
Data
  May be unstructured or structured:
    Stream of bytes (even if stored as blocks)
    Records are collections of related fields, often with a key field used for searching and sorting
  Alternate data streams (resource forks in Mac OS)

## Slide 10: Connection-Oriented Interface
Explicit open and close operations for files
  OS creates an internal data structure on open
Read and write operations use descriptor (a.k.a. handle or stream)
  Identifies the internal data structure
    No need to reparse file name
  Access permission under which file was opened
  Location of file
    Block number of start of file or inode number
  Pointer to current byte or record for sequential access

## Slide 11: UNIX File System API
create, link, unlink, createdir, rmdir
  Create file, link to file, remove link
  Create directory, remove directory
open, close, read, write, seek
  Open/close a file for reading/writing
  Seek resets current position
fsync
  File modifications can be cached
  fsync forces modifications to disk (like a memory barrier)

## Slide 12: Storage Devices
Magnetic disks
  Storage that rarely becomes corrupted
  Large capacity at low cost
  Block level random access
  Slow performance for random access
  Better performance for streaming access
Flash memory
  Storage that rarely becomes corrupted
  Capacity at intermediate cost (50x disk)
  Block level random access
  Good performance for reads; worse for random writes

## Slide 13: Magnetic Disk

## Slide 14
Left-to-right:
Single 14-inch disk platter, 16 MB removable cartridge disk for 1980s rack-mount Ampex DFR-900 series HDD, 3600 rpm, 30 ms avg. seek time
Three 5.12-inch (5.25-inch FF) platters, 19.2 GB internal drive, Quantum Bigfoot TS19A011, 4000 rpm, 10.5 ms seek
Four 3.74-inch (3.5-inch FF) platters, likely 80 GB internal drive, Seagate Barracuda, 7200 rpm, 8 ms seek
Single 2.56-inch (2.5-inch FF) platter, 10.06 GB internal drive, IBM Travelstar 07N5138, 4200 rpm, 12 ms seek

## Slide 15
Notes: Head and track are not to scale – head is actually much much bigger than a track.
Track ~ 1 micron wide
  Wavelength of light is ~ 0.5 micron
  Resolution of human eye: 50 microns
  Outer edge of disk is travelling at 30 mph, with the head riding on top of the disk surface with a cushion of a few atoms

## Slide 16: Disk Tracks
~ 1 micron wide
  Wavelength of light is ~ 0.5 micron
  Resolution of human eye: 50 microns
  100K tracks on a typical 2.5” disk
Separated by unused guard regions
  Reduces likelihood neighboring tracks are corrupted during writes (still a small non-zero chance)
Track length varies across disk
  Outside: More sectors per track, higher bandwidth
  Disk is organized into regions of tracks with same # of sectors/track
  Only outer half of radius is used
    Most of the disk area in the outer regions of the disk

## Slide 17: Sectors
Sectors contain sophisticated error correcting codes
  Disk head magnet has a field wider than track
  Hide corruptions due to neighboring track writes
Sector sparing
  Remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
Track skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential ops
Notes: Error correcting code: ex: parity. But you can get more sophisticated.

## Slide 18: Disk Performance
Disk Latency =
  Seek Time + Rotation Time + Transfer Time
  Seek Time: time to move disk arm over track (1-20ms)
    Fine-grained position adjustment necessary for head to “settle”
    Head switch time ~ track switch time (on modern disks)
  Rotation Time: time to wait for disk to rotate under disk head
    Disk rotation: 4 – 15ms (depending on price of disk)
    On average, only need to wait half a rotation
  Transfer Time: time to transfer data onto/off of disk
    Disk head transfer rate: 50-100MB/s (5-10 usec/sector)
    Host transfer rate dependent on I/O connector (USB, SATA, …)

## Slide 19: Toshiba Disk (2008)

## Slide 20: Question
How long to complete 500 random disk reads, in FIFO order?

## Slide 21: Question
How long to complete 500 random disk reads, in FIFO order?
  Seek: average 10.5 msec
  Rotation: average 4.15 msec
  Transfer: 5-10 usec
500 * (10.5 + 4.15 + 0.01)/1000 = 7.3 seconds

## Slide 22: Question
How long to complete 500 sequential disk reads?

## Slide 23: Question
How long to complete 500 sequential disk reads?
  Seek Time: 10.5 ms (to reach first sector)
  Rotation Time: 4.15 ms (to reach first sector)
  Transfer Time: (outer track)
    500 sectors * 512 bytes / 128MB/sec = 2ms
Total: 10.5 + 4.15 + 2 = 16.7 ms
  Might need an extra head or track switch (+1ms)
  Track buffer may allow some sectors to be read off disk out of order (-2ms)

## Slide 24: Question
How large a transfer is needed to achieve 80% of the max disk transfer rate?

## Slide 25: Question
How large a transfer is needed to achieve 80% of the max disk transfer rate?
  Assume x rotations are needed, then solve for x:
  0.8 (10.5 ms + (1ms + 8.5ms) x) = 8.5ms x
Total: x = 9.1 rotations, 9.8MB

## Slide 26: Disk Scheduling
FIFO
  Schedule disk operations in order they arrive
  Downsides?

## Slide 27: Disk Scheduling
Shortest seek time first
  Not optimal!
    Suppose cluster of requests at far end of disk
  Downsides?

## Slide 28: Disk Scheduling
SCAN: move disk arm in one direction, until all requests satisfied, then reverse direction
Also called “elevator scheduling”

## Slide 29: Disk Scheduling
CSCAN: move disk arm in one direction, until all requests satisfied, then start again from farthest request

## Slide 30: Disk Scheduling
R-CSCAN: CSCAN but take into account that short track switch is < rotational delay

## Slide 31: Question
How long to complete 500 random disk reads, in any order?

## Slide 32: Question
How long to complete 500 random disk reads, in any order?
  Disk seek: 1ms (most will be short)
  Rotation: 4.15ms
  Transfer: 5-10usec
Total: 500 * (1 + 4.15 + 0.01) = 2.2 seconds
  Would be a bit shorter with R-CSCAN
  vs. 7.3 seconds if FIFO order

## Slide 33: Question
How long to read all of the bytes off of a disk?

## Slide 34: Question
How long to read all of the bytes off of a disk?
  Disk capacity: 320GB
  Disk bandwidth: 54-128MB/s
Transfer time =
  Disk capacity / average disk bandwidth
  ~ 3500 seconds (1 hour)

## Slide 35: Device Intelligence
Disk and flash devices now have simple CPUs
  Disk head scheduling, remapping, SSD write leveling
Historical trends based on technological ratios
  I/O channels and disk controllers in 1960s had a fair amount of processing power since the main CPU was expensive, e.g., independent searching for a file record given a key
  When CPU costs decreased, I/O devices became dumb so that you could build a cheaper overall system => OS file system did more work
  Now, CPUs are very cheap so device manufacturers include more intelligence on devices

## Slide 36: Flash Memory

## Slide 37: Flash Memory
Writes must be to “clean” cells; no update in place
  Large block erasure required before write
  Erasure block: 128 – 512 KB
  Erasure time: Several milliseconds
Write/read page (2-4KB)
  50-100 usec

## Slide 38: Flash Drive (2011)

## Slide 39: Question
Why are random writes so slow?
  Random write: 2000/sec
  Random read: 38500/sec

## Slide 40: Flash Translation Layer
Flash device firmware maps logical page # to a physical location
  Garbage collect erasure block by copying live pages to new location, then erase
    More efficient if blocks stored at same time are deleted at same time (e.g., keep blocks of a file together)
  Wear-levelling: only write each physical page a limited number of times
  Remap pages that no longer work (sector sparing)
Transparent to the device user

## Slide 41: File System – Flash
How does Flash device know which blocks are live?
  Live blocks must be remapped to a new location during erasure
TRIM command
  File system tells device when blocks are no longer in use

## Slide 42: File System Workload
File sizes
  Are most files small or large?
  Which accounts for more total storage: small or large files?

## Slide 43: File System Workload
File sizes
  Are most files small or large?
    SMALL
  Which accounts for more total storage: small or large files?
    LARGE

## Slide 44: File System Workload
File access
  Are most accesses to small or large files?
  Which accounts for more total I/O bytes: small or large files?

## Slide 45: File System Workload
File access
  Are most accesses to small or large files?
    SMALL
  Which accounts for more total I/O bytes: small or large files?
    LARGE

## Slide 46: File System Workload
How are files used?
  Most files are read/written sequentially
  Some files are read/written randomly
    Ex: database files, swap files
  Some files have a pre-defined size at creation
  Some files start small and grow over time
    Ex: program stdout, system logs

## Slide 47: File System Design
For small files:
  Small blocks for storage efficiency
  Concurrent ops more efficient than sequential
  Files used together should be stored together
For large files:
  Storage efficient (large blocks)
  Contiguous allocation for sequential access
  Efficient lookup for random access
May not know at file creation
  Whether file will become small or large
  Whether file is persistent or temporary
  Whether file will be used sequentially or randomly

## Slide 48: File System Abstraction
Directory
  Group of named files or subdirectories
  Mapping from file name to file metadata location
Path
  String that uniquely identifies file or directory
  Ex: /cse/www/education/courses/cse451/12au
Links
  Hard link: link from name to metadata location
  Soft link: link from name to alternate name
Mount
  Mapping from name in one file system to root of another

## Slide 49: Directory Levels
 | System-wide | Per-device
Flat |  | CP/M
Two-level | OS/360 – top-level is user name | 
Tree-structured | UNIX | Windows

## Slide 50: Path Names
Absolute path
  Fully qualified
  Starts at root (“/” in Unix systems)
Relative path
  Partially qualified, ex: public_html/3220.html
  Unqualified, ex: 3220.html
  Starts at current working directory
  . = this directory, .. = parent directory

## Slide 51: File Types
Extension identifier (.c, .o)
  Can be used to specify usage or structure
  OS can associate a specific application with an extension
Magic number within file
  Identify usage or structure
  First four bytes for ELF file are: 177 E L F

## Slide 52: File Types (2)
Regular file
  Text (e.g., ASCII)
  Binary
Directory
  Writes must be restricted to preserve structure
Special file
  Maps physical I/O device to the file system

## Slide 53: File Types (3)
UNIX philosophy as stated by Ritchie and Thompson (inventors):
  “the structure of files is controlled by the programs that use them, not by the system”
Alternate approach, e.g., IBM z/OS
  “An access method defines the technique that is used to store and retrieve data. Access methods have their own data set structures to organize data, macros to define and process data sets, and utility programs to process data sets.”
    Ex: Virtual Sequential Access Method (VSAM)
    Ex: Queued Sequential Access Method (QSAM)